CCore on BeagleBone Black

Sergey Strukov 2014, version 1.00

Copyright © 2014 Sergey Strukov. All rights reserved.
This document is public. You may freely distribute it free of charge as far as it's content, copyright notice and authorship is unchanged.
## 1. Introduction.
Since the version 1.08 CCore includes the target for the popular board BeagleBone Black. You can use this target to build applications running on this board. See the site http://beagleboard.org/black for a comprehensive source of information about this hardware. The board is a small card with low power consumption (it may run on USB-supplied power), but with rich hardware capabilities. In fact, it may be used as a fully-featured PC, been connected with the monitor, keyboard and mouse.
To start working with the board unpack it and simply connect to the USB port on the host PC. The board is shipped with the pre-installed Linux distribution. Once connected the Linux kernel is started and the board is recognized by PC as the flash drive. The on-board flash has two partitions. The first one is formatted as a FAT drive and contains two-stage bootloader. This partition is seen over USB, so you can change its files from PC. The bootloader consists of the three files: MLO, u-boot.img and uEnv.txt files. The first file is the first stage bootloader. It starts first after the power on. Then it boots the second-stage bootloader u-boot.img, which is the u-Boot bootloader (see the product site http://www.denx.de/wiki/U-Boot). The second-stage bootloader finally boots the Linux kernel. But you can alter its behavior by changing the file uEnv.txt. This file contains a script, executed by the bootloader. You may change it to instruct the bootloader to download and run an image using the TFTP protocol from the host PC. Here is the script to do so:
uenvcmd=setenv ipaddr 192.168.99.10;setenv serverip 192.168.99.1;tftpboot 81000000 bootfile;go 81000000
The first IP address is the address of the board itself. The second is the IP address of the TFTP server. bootfile is the name of the file from the server to be downloaded. You must connect the board with PC by the Ethernet cable (directly or using switch). Configure the PC Ethernet card with the proper IP address manually (you may choose any other suitable address). You must run the TFTP server on the host PC. Then reapply a power to the board. It will download and run the image from the host PC using the TFTP protocol.
You may also boot the board from a standalone SD memory card. All you need is a memory card, this card must contain an active FAT partition with these three files in the root directory. Insert the card into the card pocket on the device and turn the power on.

## 2. Building a CCore application.
To build a CCore application you need a cygwin (or cygwin64), a toolset and a CCore installation. You can build the toolset yourself. Read the CCore supplied documentation about the building process and environment.
Here is the target files layout:
CCore
  ...
obj
  ...
sysroot
  lib
    ...
  obj
    ...
  src
    ...
  usr
    ...
  Makefile
test
  ...
test-obj
  ...
tools
  Boot
    ...
  BootServer
    ...
  ELFtoUboot
    ...
  HowToBuild
    ...
  Makefile
Two important directories are: sysroot and tools. The first is the sysroot part of the gcc cross-compiler. It is required to build the cross-compiler and to link applications. Once you have the cross-compiler you must build libraries libc.a and libm.a and the startup file crt0.o. The Makefile in this directory is doing it. You may need to alter it to give proper paths to the cross-compiler and tools. The tools contains tree important tools. You must build them to use CCore. Use the Makefile in this directory to build. Boot is the boot utility, it can boot ELF image over an Ethernet link to the board once the board runs BootServer. ELFtoUboot is a converter, it takes an ELF image and creates a raw file, this file can be run on the board using a TFTP server.
The following is the step-by-step description of the CCore deployment on Windows64 and cygwin64.
First you need the following hardware: host PC, BeagleBone Black board, Ethernet link between the host PC and the board. Configure the Ethernet card on PC, connected with the board to the IP address 192.168.99.1 and the IP subnet mask 255.255.255.0. Then plug the board to the USB connector on the PC. Wait until the Linux is running (you will see flashing board lights). PC will detect the new USB memory storage device. Go to this drive, find the file uEnv.txt and edit it as shown above. Reapply power to the board. It will try to download and run an image from the host PC using the TFTP protocol. If you wish to start the Linux again, you have to download and run the image with the single command
mov pc, lr
You may prepare such image using assembler, linker and ELFtoUboot converter. Just remember, that the image base and the entry point is 8100'0000h.
The next step is to configure and run a TFTP server on the host PC. You may use the following one http://tftpd32.jounin.net . Once it is done, you is able to download and run CCore images. The board requests the file bootfile from the server. Such files are created from ELF images by the utility ELFtoUboot.
The next step is the installation of the CCore itself. But first you need to install cygwin64. Go to the product site https://cygwin.com for the software. You must include make, bash and gcc in your installation. You also need libgmp-devel component. Once you have the cygwin installed, go to the home directory and create the subdirectory bin. Include it to the cygwin search path. This place is used to store host utilities. Finally, obtain and unpack the CCore release. Do it under your home directory, avoid file and directory names with the space. Go to the CCore root directory. Make the following adjustments here: copy the file Makefile.WIN64 to the Makefile and edit the file Makefile.host. Change the host target name to the WIN64:
CCORE_TARGET = WIN32
  change to
CCORE_TARGET = WIN64
You are ready to build the host CCore library and tools. Just issue the command make in the CCore root directory from the cygwin console (not the Windows console).
The next step is to build the cross-toolchain. The simplest way is to get it from the github repository https://github.com/SergeyStrukov/CCoreOpt-Beagle. Or you can build it yourself, but the process is tedious. You will need the subdirectory sysroot during the build process. You may also find a build brief in the subdirectory tools/HowToBuild.
Once you have the cross-toolchain ready, you can build the target CCore library and tools. Go to the target directory CCORE_ROOT/Target/BeagleBoneBlack. Check the tool paths in the file Makefile.tools. To build the CCore just issue the command make. To build tools go to the subdirectory tools and issue the command make. You are done.
When everything is ready you can build and run CCore applications on the board. There are two ways to run a built application. The result of the linker stage is an ELF file. You can convert it to a raw image and download and run using a TFTP server as described above. The utility ELFtoUboot should be called as following:
ELFtoUboot.exe <ELF-file> <boot-file>
Or you can run the PTP boot server on the board. This server is built in the directory tools/BootServer. You can run it using the first method. Then you can use the boot client (tools/Boot) to boot an ELF file:
BeagleBoot.exe r 192.168.99.10 <ELF-file>
Both ELFtoUboot.exe and BeagleBoot.exe are created in your HOME/bin directory. The IP address is hardcoded in the boot server, so if you wish to use another one, change tools/BootServer/main.cpp and rebuild the boot server.
## 3. Hardware resource utilization.
A CCore application is running in a privilege non-secure mode, so you have a full access to any board hardware. Briefly after start it turns on the MMU and caches, so you have a maximum CPU performance. It sets also the CPU clock to 600 MHz. It is possible to increase the clock up to 1 GHz, but it requires the reprogramming the power supply device to increase the CPU core voltage and is not implemented in this version. MMU is programmed to map a virtual address to the physical but such a way, that the physical address is always equal to the virtual. It also specifies memory cache attributes to various memory regions.
The board has 512 MByte DDR memory, this memory is visible at the address range 0x8000'0000 – 0xA000'0000. A CCore application image is loaded and started from the address 0x8100'0000. The memory is divided on several memory regions with different usage purpose. The first region 0x8000'0000-0x8080'0000 is reserved for the video-memory. It has no-cache attributes. The next region 0x8080'0000-0x8100'0000 is reserved for the shared memory heap. It also has no-cache attributes. This memory is used to exchange data with peripheral devices without a manual memory cache control. For example, Ethernet packet descriptors and data buffers are resides in this memory region. Right after this region an application image begins. It's assumed to be several MBytes length. After the image (which contains the code and static variables) the free memory zone begins. This zone is used to allocate a space for the prime task stack (1 MByte), the interrupt stack (1 MByte), the interrupt heap (1 MByte), the system log (16 MBytes) and the heap (204 MBytes). All these memory regions have the full cache attributes. If the application image length is less than 16 MBytes, only the first 256 MBytes half of the memory is used.
The following on-chip devices are reserved for system use and should not be touched by any other software entities: GPIO1, DMTimer2, DMTimer4, WDTimer, INTC (interrupt controller). You may use only functions, provided by the target to work with these devices.
The following on-chip devices must be used under the ControlMutex protection: PRMC and Control Module. The mutex is declared in the file dev/DevControlMutex.h.
namespace CCore {
namespace Dev {

/* global ControlMutex */

extern Mutex ControlMutex;

} // namespace Dev
} // namespace CCore
## 4. Hardware support classes.
The target contains several classes to work with peripheral devices.
### 4.1 RegRW – read/write registers (dev/DevRW.h).
The class RegRW should be used to read/write registers. It can be used along or with Regen-generated bar-classes.
namespace CCore {
namespace Dev {

/* types */

typedef uint32 AddressType;

/* classes */

class RegRW;

/* class RegRW */

class RegRW
 {
   AddressType base_address;

  public:

   explicit RegRW(AddressType base_address);

   template <class UInt>
   UInt get(uint32 address);

   template <class UInt>
   void set(uint32 address,UInt value);
 };

} // namespace Dev
} // namespace CCore

Constructor takes a base address of a register bar as the argument. Then you can use methods set() and get() to read or write registers. The template parameter must be one of uint8, uint16, or uint32. The class should be used to avoid register operations reordering.

### 4.2 Interrupt handling (dev/DevIntHandle.h).
The following family of functions can be used to setup an interrupt handler for a particular source.
namespace CCore {
namespace Dev {

/* enum IntSource */

enum IntSource
 {
  Int_LCDCINT = 36,
  Int_I2C0INT = 70,
  Int_I2C1INT = 71,
  Int_I2C2INT = 30,
  Int_TINT4 = 92,

  Int_3PGSWRXTHR0 = 40,
  Int_3PGSWRXINT0 = 41,
  Int_3PGSWTXINT0 = 42,
  Int_3PGSWMISC0 = 43,

  Int_GPIO1_0 = 98,
  Int_GPIO1_1 = 99,

  Int_TableLen = 128
 };

/* functions */

void SetupIntHandler(IntSource int_source,
        Function<void (void)> handle_int,
        unsigned priority=0); // priority 0-63

void CleanupIntHandler(IntSource int_source);

void EnableInt(IntSource int_source);

void DisableInt(IntSource int_source);

} // namespace Dev
} // namespace CCore

SetupIntHandler() connects the given interrupt handler with the given interrupt source. The third argument is the priority, if several interrupts are active simultaneously, then the more prioritized handler calls first. The highest priority is 0. After call of this function interrupts from the source are enabled.
CleanupIntHandler() disconnects the interrupt handler from the given source.
EnableInt() enables the interrupt from the given source.
DisableInt() disables the interrupt from the given source.
IntSource is an enumeration which designates interrupt sources. It is not the full list of all available interrupts on this CPU. For the full list read the chip documentation.
An interrupt handler is a normal function. This function is called in the interrupt context. So there are limitations on what the function can do. In particular, it must be quick and cannot call any blocking functions. It cannot use the default heap or print to the console, but can use the interrupt heap. For synchronization objects it must call only methods, allowed in the interrupt context, usually such methods have names, ended with the “_int” suffix.

### 4.3 Lights control (dev/DevLight.h).
The are four lights on the board. You can control them by the following set of functions.
namespace CCore {
namespace Dev {

/* functions */

void LightSet(unsigned mask); // 4 lsb

void LightOn(unsigned mask); // 4 lsb

void LightOff(unsigned mask); // 4 lsb

void LightToggle(unsigned mask); // 4 lsb

} // namespace Dev
} // namespace CCore

LightSet() sets the lights according the given mask.
LightOn() turns on the lights according the given mask. I.e. if some bit is not set, the correspondent light remains unchanged. Other are lighted.
LightOff() turns off the lights according the given mask. I.e. if some bit is not set, the correspondent light remains unchanged. Other are darken.
LightToggle() toggles the lights according the given mask. I.e. if some bit is set, the correspondent light changes, otherwise it remains unchanged.
A mask has 4 lowest bits significant.

### 4.4 Performance counters (dev/DevPerfCount.h).

### 4.5 I2C controller (I2CDevice.h).

### 4.6 Video device (video/VideoControl.h).

### 4.7 Ethernet controller (dev/DevEth.h).